## Slide 1: Internship Project GPS Tracker
Final Presentation
Final Buld and Improvements

## Slide 2: Functionality
This project aims to build a portable and battery efficient GPS tracker that sends out its location through a GSM or GPRS interface, thus being able to send the GPS coordinates of its location to the user either by SMS or by updating a web-rendered map.
This module will have 2 functioning states: SLEEP mode in which the GPS tracker will aim to consume the least amount of power as possible. This state is useful for when the tracker remains still for extended periods of time. The other state, GET_GPS, is being used when the module is in motion and will send its GPS coordinates to the user.

## Slide 3: Modules used
The GPS tracker will be built around these three main modules:
I: MCHP AVR128DA48 μController- main processing unit which communicates with the other modules and controls them.
II: SIMCOM SIM808 GSM/GPRS+GPS module – the main communication interface with the outside world, being able to extract its exact GPS coordinates and access GSM/GPRS networks using a SIM card.
III: BOSCH BMI160 accelerometer – this module can sense sudden movements, thus alerting the μC when the tracker is being moved. We are allowing the tracker to remain in its lowest power consumption mode while it is not moving.
Due to stock shortages, this part had been swapped with STM LIS331DLH Accelerometer

## Slide 4: Project Timeline
GPS TRACKER PROTOTYPE: In this stage of the project we will sacrifice the aspect of portability and power efficiency in hopes of a faster development. We will use the available shields for each module for their quick plug-and-play capabilities(AVR CURIOSITY NANO+CURIOSITY NANO ADAPTER for the AVR128DA48 microcontroller, 6DOF IMU 2click shield for the BMI160 and a standard shield for the SIM808 module).
This is the stage where the project is currently at.

## Slide 5: GPS TRACKER HW PROTOTYPE BLOCK SCHEMATIC
Connections made between the 3 shields.

## Slide 6: HW Prototype
-6DOF IMU 2click
-AVR128DA48 Curiosity nano
SIM808 Breakout Shield

## Slide 7: Software Architecture Prototype
Flowchart diagram of the software architecture loaded on the microcontroller

## Slide 8: Next goals for GPS TRACKER PROTOTYPE stage
Fully integrate GPRS communication (currently main communication is made through GSM with SMS text messages)
Achieve full communication with a web-site that will store the current and previous GPS coordinates into a database.
Improve readability of the software.

## Slide 9: Goals for the next project stages
GPS TRACKER HW and PCB design
  Achieve better power efficiency by stripping out unnecessary components.
  Integrate battery charging functionality
  Build a compact and portable PCB board
GPS TRACKER BETA+TUNE UP
  Improve software efficiency
  Fix any software bugs or hardware errors
  Build a user-friendly GUI for the web-site (can be done later)

## Slide 10: GPS TRACKER HW and PCB design
In this stage a fully functioning HW PCB design has been achieved, which is more portable and easier to use than the HW Prototype built using breakout shields.
Due to several constraints, the portability factor is not fully achieved, but the HW proved to have excellent RF performance and acceptable power consumption.

## Slide 11: GPS TRACKER HW Schematic

## Slide 13: GPS TRACKER PCB Layout
TOP Layout
BOTTOM Layout

## Slide 14: GPS TRACKER Final PCB

## Slide 15: GPS Tracker Web Application
The Application is built using PHP + MySQL for the Back-End in order to store the GPS coordinates sent out by the tracker.
For the Front-End we use HTML, CSS and JS. Using Google’s GMAP JS API, we can render the route taken by the tracker on the World Map using the previously mentioned MySQL Database.
The Server is Hosted using AWS(Amazon Web-Services).

## Slide 16: First Page

## Slide 18: Functionality

## Slide 19: Thank You!
Bitbucket Repo
Web Application